NB
- We use Point3 and Colour as an alias for Vec3.
 - Point3 is used to designate a position in space. - Vec3 is used for shifting points around or calculating the distance between them.
This is worth reminding yourself about when reading code.
We use a viewport and place it between our eye (i.e. camera) and the scene. Our output image is like a blank canvas where we need to determine a colour for each pixel.
For each pixel, we map it to a location on the viewport.
We then calculate the colour of the ray endpoints as they land on the viewport. This colour is then applied to the pixel on the final output image.

---
Aspect Ratio = 16/9 = 1.78
Viewport Height = 2.0
Veiwport Width = (2.0 * 1.78) = 3.56
Focal Length = 1.0
Horizontal Vector = Vec3(3.56,0,0)
Vertical Vector = Vec3(0,2,0)
Lower Left Corner = Origin – (Horizontal Vector / 2) – (Vertical Vector / 2) – Vec3(0, 0, Focal Length)
Lower Left Corner = Point3(0,0,0) – Vec3(1.78,0,0) – Vec3(0,1,0) – Vec3(0,0,1) = Point3(-1.78,-1,-1)
Now we can take any pixel on the output image (which starts out blank like a canvas) and calculate it’s relative position on the viewport (using U and V which are fractions of the Horizontal and Vertical Vectors). Once we determine the colour at that location on the viewport (by sending a ray to that point), we make the pixel that colour on our output image.
E.g. if the image is 400 x 224 pixels, then pixel (160,100) would be located on the viewport at:
Vw = 3.56
u
v
Vh = 2.0
LLC
(-1.78,-1,-1)
y
-z
Fl = 1.0
(0,0,0)
x
U = (160/400) Horizontal Vector = 0.40 Vec3(3.56,0,0) = Vec3(1.42,0,0)
V = (100/224) Horizontal Vector = 0.45 Vec3(0,2,0) = Vec3(0,0.9,0)
Ray EndPoint = LLC + U + V = Point3(-1.78,-1,-1) + Vec3(1.42,0,0) + Vec3(0,0.9,0) = Point3(0.53,-0.1,-1 )